## Slide 1: F-16 Model
Linear model has form
Contains all dynamics around an operating (trim) point
Is defined by matrices A, B, C, and D
Non-linear model has form
In this case function f is called nlplant
  In Simulink it is contained in a Matlab function block
  Source is a C-function (nlplant.c)
  Compiled into Mex-function (mex nlplant.c)
Linear vs. Non-linear models

## Slide 2: F-16 Model
Model has 12 “core” states (x) which need to be integrated
  North position
  East position
  Altitude
  Bank angle φ
  Pitch angle θ
  Heading angle ψ
  Total airspeed V
  Angle of attack α
  Sideslip angle β
  Roll rate p
  Pitch rate q
  Yaw rate r
States

## Slide 3: F-16 Model
Model has 6 “auxilliary” states
  Mostly 1st order dynamics
    Gain usually 1
  Engine thrust dynamics
  Elevator actuator
  Aileron actuator
  Rudder actuator
  Leading edge flap
    2 internal states
    Not used in low fidelity model
Total of 18 states in linear & non-linear model
States
18

## Slide 4: F-16 Model
Model has 4 pilot inputs
  Thrust [lbf]
    Range from 1000 to 19000
  Elevator angle [deg]
    Range from -25° to +25°
  Aileron angle [deg]
    Range from -21.5° to +21.5°
  Rudder angle [deg]
    Range from -30° to +30°
Linear model only has these inputs (B matrix size = 18 x 4)
  Are passed through the first order actuator dynamics before going to the aerodynamic part of the model
  Non-linear model is different
Inputs

## Slide 5: F-16 Model
Non-linear model (nlplant function) has 18 inputs
  12 “core” states
  Thrust (after dynamics!)
  Elevator angle (after dynamics!)
  Aileron angle (after dynamics!)
  Rudder angle (after dynamics!)
  Leading edge flap angle (keep at zero)
  Fidelity switch (keep at zero for lofi)
Inputs non-linear model
18

## Slide 6: F-16 Model
Linear and non-linear model have 18 outputs
  12 “core” states
  Longitudinal load factor nx
  Lateral load factor ny
  Vertical load factor nz
  Mach number
  Dynamic pressure qbar
  Static pressure ps
Linear model’s C matrix has size 18 x 18
  Outputs are deviations from trim point
Output from nlplant function has size 18
  12 “core” state derivatives to be integrated
  6 “quasi” derivatives that are really outputs
Outputs
18